Network Security
Sample Final 1
x: 2 4 8
1a. A checksum is a value that will check the integrity of the data. Without doing a checksum then it is possible that data has been altered.
1b. TLS_DHE_RSA_WITH_AES_128_CBC_SHA
This cipher suite describes TLS using Diffie Hellman Ephemeral for forwad secrecy using RSA algorithm. The message is encrypted with 128 bit AES with the cipher block chaining mode. Finally it is hashed with Sha for integrity.

3.

# Internet to DMZ FW
iptables -t FILTER -A INPUT -protocol tcp -s 10.30.111.3 -i eth1 -j ACCEPT -m conntrack -cstate NEW, ESTABLISHED
iptables -t FILTER -A OUTPUT –protocol tcp -s 30.10.111.2 - -i eth0 -j ACCEPT -m conntrack -cstate ESTABLISHED

iptables -t FILTER -A INPUT -protocol tcp -s 10.30.111.3 -i eth1 -dport 80 -j ALLOW -m conntrack -cstate ESTABLISHED
iptables -t FILTER -A INPUT -protocol tcp -s 10.30.111.3 -i eth1 -dport 22 -j ALLOW -m conntrack -cstate ESTABLISHED
iptables -t FILTER -A INPUT -protocol udp -s 10.30.111.3 -i eth1 -dport 53 -j ALLOW -m conntrack -cstate ESTABLISHED

iptables -t FILTER -A INPUT -protocol tcp -s 10.30.111.3 -i eth1 -j DROP -m conntrack -cstate ESTABLISHED

# DMZ to Internal FW
iptables -t FILTER -A INPUT -protocol tcp -s 10.20.111.0 -sport 80 -j DROP

iptables -t FILTER -A INPUT -protocol tcp -s 10.10.111.3 -i eth1 -j ACCEPT -m conntrack -cstate ESTABLISHED
iptables -t FILTER -A OUTPUT –protocol tcp -s 10.10.111.2 - -i eth0 -j ACCEPT -m conntrack -cstate ESTABLISHED

5a. The attacker would need to be able to inspect a packet and set up a rogue dhcp server. They can do it when joining a network a host will send a discover packet to the dhcp server indicating it needs an IP address. An attacker can listen for this discover packet and the rogue dhcp server can send an offer packet. If the poisoned offer packet reaches the client before the valid server’s packet then the client will use the rogue dhcp server and the mitm attack succeeds.

5b. A dhcp starvation packet can be used where an attacker can send many discover packets so that the dhcp server runs out of ip addresses.

5c. One method to prevent dhcp attacks is to use the cam table where an ip address is associated with a Mac adress

7. Trudy can bypass MAC address filtering by spoofing their MAC address with an approved mac address.
7c. Trudy can connect to the rogue