## Slide 1: 802.11 Security
Review of Wi-Fi
Sniffing Wi-Fi
WEP
802.11i

## Slide 2: Objectives
Describe how WEP is flawed and work out various methods to attack it
Explain how WEP Encryption and Decryption works
Understand how WPA and WPA2 improves upon WEP
Describe methods to attack any wireless network
Understand Wifi-Protected Setup

## Slide 3: IEEE 802.11 Wireless LAN
802.11b
  2.4-2.495 GHz unlicensed radio spectrum
  up to 11 Mbps
  direct sequence spread spectrum (DSSS) in physical layer: all hosts use same chipping code
  Deprecated in 2004
802.11a
  5 GHz range (4915-5815MHz)
  up to 54 Mbps
  Physical layer: orthogonal frequency division multiplexing (OFDM)
    Used for encoding data on multiple frequencies
802.11g
  2.4-2.495 GHz range
  up to 54 Mbps
  OFDM
802.11n
  2.4-2.495 GHz & 4.915-5.825 GHz
  20/40 MHz channel size
  up to 600 Mbps
  OFDM
802.11ac
  2.4-2.495 GHz & 4.915-5.825 GHz
  80/160 MHz channel size
  up to 1.3 Gbps
  OFDM
All have collusion avoidance using CSMA/CA
All have base-station and ad-hoc versions
All allow for reducing bit rate for longer range

## Slide 4: 802.11 LAN architecture
wireless host communicates with base station
  Access Point (AP) = base station
  Basic Service Set (BSS) is the set of AP and STAs communicating with each other
  All AP/BSS are named by their BSSID, or MAC Address
Infrastructure mode contains:
  Stations (STA): Hosts
  Access Points (AP): Base Stations
ad hoc mode
  Hosts only
  No AP
BSSID 1
BSSID 2
Internet
hub, switch
or router
AP
AP
SSID

## Slide 5: Channels, beacon frames & association
802.11b/g/n
    2.4GHz-2.495GHz spectrum divided into 13 channels (14 in Japan) at different frequencies; 3 non-overlapping (4 in Japan)
    AP admin chooses frequency for AP
    Interference possible: channel can be same as that chosen by neighboring AP! 2.4 GHz is also popular for other appliances such as wireless telephones and microwaves
AP regularly sends beacon frame
    Includes SSID (Network Name), BSSID (AP MAC), beacon interval (often 0.1 sec)
host: must associate with an AP
    scans channels, listening for beacon frames or sends a probe request
    selects AP to authenticate and associate with
    Authentication may be Open, WEP, WPA, WPA2
    Association is to join the network
    After joining, host will typically run DHCP to get IP address in SSID or Network subnet
    Host will keep IP if it travels from one AP to another within the same SSID/Network

## Slide 6: 802.11 frame: addressing
frame
control
duration
address
1
address
2
address
4
address
3
payload
CRC
2Bytes
2
6
6
6
2
6
0 - 2312
4
seq
control
Address 2: Source. MAC address of wireless host or AP transmitting this frame
Address 1: Destination. MAC address of wireless host or AP to receive this frame
Address 3: MAC address
of router interface to which AP is attached
Address 4: used only in ad hoc mode

## Slide 7
Internet
router
AP
H1
R1
H1 MAC addr AP MAC addr R1 MAC addr
address 1
address 2
address 3
802.11 frame
H1 MAC addr R1 MAC addr
dest. address
source address
802.3 frame
802.11 frame: addressing to STA

## Slide 8
Internet
router
AP
H1
R1
AP MAC addr H1 MAC addr R1 MAC addr
address 1
address 2
address 3
802.11 frame
R1 MAC addr H1 MAC addr
dest. address
source address
802.3 frame
802.11 frame: addressing to AP

## Slide 9
Internet
router
AP
H1
R1
? ? ?
address 1
address 2
address 3
802.11 frame
R A
dest. address
source address
802.3 frame
Exercise: Suppose you see a Ethernet frame to Router R from AP A. You know that the frame was originally from Host H1. What are the three addresses of the 802.11 frame?

## Slide 10: 802.11 frame (more)
Type
From
AP
Subtype
To
AP
More
frag
WEP
More
data
Power
mgt
Retry
Rsvd
Protocol
version
2 Bits
2
4
1
1
1
1
1
1
1
1
frame
control
duration
address
1
address
2
address
4
address
3
payload
CRC
2 Bytes
2
6
6
6
2
6
0 - 2312
4
seq
control
frame:
frame control field expanded
Protocol version: Always zero
Type/subtype distinguishes beacon, association, ACK, RTS, CTS, etc frames.
To/From AP defines meaning of address fields
802.11 allows for fragmentation at the link layer but is almost only ever used during an attack since 802.3 (Ethernet) frames are smaller
Retry identifies retransmitted frames (e.g., when ACK lost)
802.11 allows stations to enter sleep mode
WEP = 1 if WEP encryption is used

## Slide 11: 802.11 Sniffing
Requires wireless card that supports raw monitoring mode (rfmon)
    Grabs all frames including management frames
Tools:
    There are many. Dump packets into Wireshark; interfaces with GPS devices, storing physical location
Access control lists based on MAC addresses
    Do they work?
      Attacker sniffs channel, obtains valid MAC address
      Attacker modifies its MAC address to valid address
  DEFCON Wi-Fi Shootout
      Read Wi-Fi traffic from 125 miles away
      They had to adjust for the curvature of the earth
      FCC max allowable transmit powers are 1watt indoors, 4 watt outside

## Slide 12: Firewalled Networks with Wi-Fi (1)
Firewall blocks traceroutes,…
Traffic sent by wireless hosts/APs not blocked by firewall
  Leaking of internal information
Trudy can traceroute and port scan through AP
  Establish connections
  Attempt to overtake
External Network

## Slide 13: Firewalled Networks with Wi-Fi (2)
Move AP outside of firewall?
  Trudy can no longer tracetroute internal network via AP
  But Trudy still gets everything sent/received by wireless hosts
External Network

## Slide 14: Firewalled Networks with Wi-Fi (3)
Crypto at link layer between wireless hosts and AP
  Crypto provides authentication and confidentiality by implementing WEP/WPA/WPA2
  Trudy doesn’t hear anything
  Trudy can not port scan
  Wireless hosts can access internal services
External Network

## Slide 15: Sniffing Encrypted 802.11 traffic
Suppose:
Traffic encrypted with symmetric crypto
Attacker can sniff but can’t break crypto
Information is still leaked:
SSID, Mac addresses
Manufacturers of cards from MAC addrs
Count # of devices
Management frames are sent in the clear
802.11w protects management frames, but is not widely implemented
Traffic analysis reveals:
  Size of packets
  Timing of messages
  Determine apps being used
But cannot see anything really useful
Attacker needs the keys!

## Slide 16: Attacks on Pre-Shared Keys (PSK)
Attacker can get keys from disgruntled employee or sloppy administration.
Possible solution: put key in hardware or software & don’t make key visible to humans.
Problems:
  Attacker gets access to equipment with key
  With good technical skills, attacker can extract key
  Ex: large corporation puts key in flash memory of all its devices
  Someone clever extracts key, publishes it on Web, destroying corporate security solution

## Slide 17: WEP Feature Goals:
Authentication
    AP only allows authorized stations to associate
Data integrity
    Data received is the data sent
Confidentiality
    RC4 Symmetric encryption, 40-bit or 104-bit keys

## Slide 18: WEP Design Goals
Symmetric key crypto
    Confidentiality
    Station authorization
    Data integrity
Self synchronizing: each packet separately encrypted
    Given encrypted packet and key, can decrypt; can continue to decrypt packets when preceding packet was lost
    Unlike Cipher Block Chaining (CBC) in block ciphers
Efficient
    Can be implemented in hardware or software
    Older APs implemented WEP in hardware

## Slide 19: WEP Keys
40 bits + 24 bit IV
or 104 bits + 24 Bit IV
Key distribution not covered in standard
Configure manually:
  At home
  Small organization with tens of users
  Nightmare in company >100 users
Four default keys: 0,1,2,3
    Four keys can be stored at once
Key 0 is initially active at AP and hosts.
Administrator tells users: “must change to key 1 before date Z”
  During transition: old key users and new key users.
  AP encrypts with old key but decrypts with both old and new.
  Node advertises its key ID in keyID field
At deadline, AP encrypts and decrypts only with new key
Four keys allow for directional key use
  AP can use different key than hosts

## Slide 20: Symmetric Stream Ciphers
Combine each byte of keystream with byte of plaintext to get ciphertext
m(i) = ith unit of message
ks(i) = ith unit of keystream
c(i) = ith unit of ciphertext
c(i) = ks(i)  m(i) ( = exclusive or)
m(i) = ks(i)  c(i)
WEP uses RC4
Each WEP frame is encrypted with a separate IV.
keystream
generator
Key+IVpacket
keystreampacket

## Slide 21: WEP encryption (1)
Sender calculates Integrity Check Value (ICV) over data
    four-byte hash/CRC for data integrity
Each side has 104-bit shared key
Sender creates 24-bit initialization vector (IV), appends to key: gives 128-bit key
Sender also appends keyID (in 8-bit field)
128-bit key inputted into pseudo random number generator to get keystream
data in frame + ICV is encrypted with RC4:
    Bytes of keystream are XORed with bytes of data & ICV
    IV & keyID are appended to encrypted data to create payload
    Payload inserted into 802.11 frame
encrypted
data
ICV
IV
MAC payload
Key ID
3 Bytes
1
4

## Slide 22: WEP encryption (2)
New IV for each frame

## Slide 23: WEP decryption overview
Receiver extracts IV
Inputs IV and shared secret key into pseudo random generator, gets keystream
XORs keystream with encrypted data to decrypt data + ICV
Verifies integrity of data with ICV
    Note that message integrity approach used here is different from the MAC (message authentication code) and signatures (using PKI).
encrypted
data
ICV
IV
MAC payload
Key ID

## Slide 24: End-point authentication w/ nonce
Nonce: number (R) used only once-in-a-lifetime
How: to prove Alice is “live”, Bob sends Alice nonce, R. Alice
must return R, encrypted with shared secret key
“I am Alice”
R
K (R)
A-B
Alice is live, and only Alice knows key to encrypt nonce, so it must be Alice!

## Slide 25: WEP Authentication
AP
authentication request
nonce (128 bytes)
IV + nonce encrypted w/ shared key
success if decrypted value equals nonce
Not all APs do it, even if WEP
is being used. AP indicates
if authentication is necessary
in beacon frame. Done before association.

## Slide 26: Exercise: Suppose Trudy is wirelessly sniffing this exchange. What information can Trudy figure out? Hint: Go back a few slides.
AP
authentication request
nonce (128 bytes)
IV + nonce encrypted w/ shared key
success if decrypted value equals nonce
Not all APs do it, even if WEP
is being used. AP indicates
if authentication is necessary
in beacon frame. Done before association.

## Slide 27: WEP is flawed
Message integrity problems
Message privacy problems

## Slide 28: WEP authentication problems
Plaintext attack
Attacker sniffs nonce, m, sent by AP
Attacker sniffs response sent by station:
    IV in clear
    Encrypted nonce, c
Attacker calculates keystream ks = m  c, which is the keystream for the IV .
Attacker then requests access to channel, receives nonce m’
Attacker forms response c’ = ks  m’ and IV
Server decrypts, matches m’ and declares attacker authenticated !

## Slide 29: Problems with Message Integrity
ICV (Integrity Check Value) supposed to provide data integrity
    ICV is a hash/CRC32 calculation, but a flawed one.
Can predict which bits in ICV change if you change single bit in data.
    Suppose attacker knows that flipping bit 3244 of plaintext data causes bits 2,7,23 of plaintext ICV to flip
Suppose attacker intercepts a frame:
    In intercepted encrypted frame, attacker flips bit 3244 in data payload and ICV bits 2,7,23
Will ICV match after decryption at the receiver?
    After decryption, cleartext bit 3244 is flipped (stream cipher)
    Also after decryption, cleartext bits 2,7, 23 also flipped.
    So cleartext ICV will match up with data!

## Slide 30: Problems with WEP confidentiality (1)
IV is 24 bits; incremented by 1 for each packet
    224 (approx 17 million) different IV values
If you know keystream for every IV, can decrypt all frames
    1500-byte keystream for all possible IVs: 23 Gbytes of storage – feasible
How do you get the keystream for an IV ?

## Slide 31: Problems with WEP confidentiality (2)
IV reuse
    With 17 million IVs and 500 full-length frames/sec, collisions start after 7 hours
    Worse when multiple hosts start with IV=0
IV reuse:
    Trudy guesses some of Alice’s plaintext d1 d2 d3 d4 …
    Trudy sniffs: ci = di  kiIV
    Trudy computes keystream kiIV =ci  di
    Next time IV is used, Trudy can decrypt!
Worse: Weak Key Attack
    For certain key values (weak keys), disproportionate number of bits in first few bytes of the keystream are determined by just a few key bits.
    As the IV cycles, wait for weak keys
    Exploit weak keys to crack the key
    Effort is only linear in key size!
Cracker script tools
    Wep_crack: okay for 40-bit key, not 104
    Wepattack: good for guessing dictionary passwords
    Aircrack-ng: requires thousands of packets but able to guess all passwords. You can generate traffic since WEP is vulnerable to an ARP reply attack, using aireplay-ng

## Slide 32: Summary of WEP flaws
One common shared key
If any device is stolen or compromised, must change shared key in all devices
No key distribution mechanism
Infeasible for large organization as approach doesn’t scale
Crypto is flawed
Early 2001: Integrity and authentication attacks published
August 2001 (weak-key attack): can deduce RC4 key after observing several million packets
AirSnort application allows casual user to decrypt WEP traffic
Crypto problems
24 bit IV to short
Same key for encryption and message integrity
ICV flawed, does not prevent adversarial modification of intercepted packets
Cryptanalytic attack allows eavesdroppers to learn key after observing several millions of packets

## Slide 33: IEEE 802.11i draft - WPA
Much stronger encryption
    TKIP (temporal key integrity protocol)
    Intended for compatibility with existing WEP Hardware
      Still uses RC4 stream cipher
    Depreciated in 2012
Extensible set of authentication mechanisms
    Employs 802.1X authentication
Key distribution mechanism
    Typically public key cryptography
    RADIUS authentication server
        distributes different keys to each user
        also there’s a less secure pre-shared key mode
WPA: Wi-Fi Protected Access
    Pre-standard subset of 802.11i

## Slide 34: TKIP: Changes from WEP
Creates a better RC4 stream by using a key mixing function before generating the RC4 stream
IV length increased to 56-bits
IV is used as a sequence counter to stop replay attacks
Secret part of encryption key changed in every packet.
Has rekeying mechanism, new keys every 216 packets
Generates different integrity and encryption key
Uses a 64-bit Message Integrity Check (MIC)
Source and destination MAC addresses appended to data before hashing
Before hashing, key is combined with data with XOR (not just a concatenation)
Computationally efficient
Much more secure than WEP!

## Slide 35: TKIP: IV Selection and Use
IV is 56 bits
  10,000 short packets/sec
      WEP IV: recycle in less than 30 min
      TKIP IV: 900 years
  Must still avoid two devices separately using same key
IV acts as a sequence counter
    Starts at 0, increments by 1
    But two stations starting up use different keys:
        MAC address is incorporated in key

## Slide 36: TKIP: Flaws
TKIP is still vulnerable to weak passphrases
IEEE recommends 20 characters or more
Tools like CoWPAtty can be used against WPA to try a dictionary attack
TKIP is no longer considered secure
    Includes WPA+TKIP and WPA2+TKIP
    WPA+AES is still considered secure

## Slide 37: IEEE 802.11i WPA2
Non-draft version of 802.11i is called WPA2
Strongest encryption to date
Uses AES, strong block cipher
Longer key, 4-way handshake between STA and AP
    Both AP and STA are authenticated
No known weaknesses with the algorithm
    Aside from bruteforcing passwords
Pre-Shared Key is still vulnerable to weak passphrase dictionary attacks and stolen client

## Slide 38: IEEE 802.11w – Protected Management Frames
Management frames were still unencrypted after WPA2 in 2004
802.11w ratified in 2009
2014: Implemented in Linux and BSD drivers used by some wireless cards. Also implemented in Windows 8. Compatibility issues can exist with older clients (Windows 7, older APs)
Mitigates an attacker from injecting malformed management frames into the network and causing a self-DOS
Protects:
    Deauthentcation, Disassociation
    Authentication handshake frames
    QoS (802.11e) frames

## Slide 39: DOS and Fuzzing Attacks
Wireless networks are still susceptible to DoS attacks
802.11w helps but most clients and networks are still vulnerable to spoofed deauthentication packets due to delayed implementation
  Ex. Alice is talking to the AP. Bob, spoofing the MAC address of the AP will tell Alice to deauthenticate. Alice will comply and immediately try to authenticate again. Bob can flood the network, targeting many people and.
Fork-in-the-Microwave
  Open a microwave door and jam something in the door catch to make it think the door is shut
  Turn it on
  DoS to all devices at the 2.4GHz range
Fuzzing attack
  Sending malformed packets to a wireless host
  Sometimes, the driver will not read the packet correctly.
  Normally the packet is dropped, sometimes the client will crash, best case is a buffer overrun

## Slide 40: 802.1x & Extensible Authentication Protocol (EAP)
Provides multiple ways to authenticate into the network
Originally for wired and PTP connections, EAP now for 802.11
Supplicant – Host trying to authenticate
Authenticator – AP communicating with Supplicant
Authentication Server – backend server which takes care of authentication by
user credentials or token
Offers mutual authentication, both Client and Authenticator are assured
EAP is the framework, many implementations exist
Wikipedia

## Slide 41: EAP
LEAP – Lightweight EAP
    Cisco propriety
    No PKI required, easy to deploy
    Flawed and vulnerable, superseded by EAP-FAST
PEAP – Protected EAP
    Stronger implementation
    Tunnels the EAP authentication and traffic in a TLS tunnel
EAP-TLS
    Certificate based authentication
Many others
The strongest EAP implementations all rely on a solid PKI deployment

## Slide 42: 802.11 IDS
IDSs for 802.11 but are limited
Signature Analysis
    Identify packets uniquely and fast
    Fragmentation packets, Replay attempts, Deauth attacks
    Stateful IDSs can group wireless frames together to look for more sophisticated attacks at cost of more resources
Trend Analysis
    Create a baseline for the network
    Alerts on anomalies, e.g., rogue AP, DOS
IPSs are not practical since malicious wireless clients can change their MACs to an authorized

## Slide 43: Securing 802.11
Use WPA2-AES with a strong passphrase
    Better yet, use a RADIUS server
Disable backwards compatibility with WEP and TKIP
Protect the physical network
Implement a robust PKI and EAP implementation
    TTLS, PEAP-EAP-TLS, EAP-FAST
Update client trusted certificates, do not use OS defaults
Run latest vendor firmware

## Slide 44: 802.11 security summary
SSID and MAC access control lists provide minimal security
WPA2 encryption is required to not radiate all traffic
  Back-end authentication server
  Public-key cryptography for authentication and master key distribution
  Using WPA2-AES and a random key, it’s take thousands of years to brute force
  Security strength is tied to the strength of the key, don’t use dictionary words or character substitutions l1k3 th!$

## Slide 45: WPA3 Security Improvements
Perfect Forward Secrecy
No more offline dictionary attacks on passphase
“Wi-Fi” Easy Connect – improved Wi-Fi Protected Setup

## Slide 46: Wi-Fi Protected Setup (WPS)
Flawed feature that allows simple network devices to easily connect to a WPA2 network
    Used for devices such as printers
Mandatory implantation to be WiFi certified
    Push-Button-Method
        User pushes a button on AP, AP waits for 2 mins
        User pushes a button (or virtual) on Enrollee
        Enrollee is authenticated if no other Enrollee attempts to authenticate within 2 minutes. Otherwise, the AP aborts
    PIN Method: 4 or 8-digit PIN
        Usually a static number on a sticker on AP

## Slide 47: WPS PIN Method
User selects WPS PIN Method, and types in PIN
8 Digit PIN Split into two halves
    First 4 Digit (10^4 possibilities)
    Second 3 Digit + 1 Checksum ( < 10^3 possibilities )

## Slide 48: WPS PIN Method (Notational)
An attacker can attempt to guess the first 4 digit PIN until correct, then move on to the second 4-digit PIN
Lockout system depends on AP, some have 1 minute lock down after failure
AP
hash(first 4-digit PIN + 128-bit random)
Confirm correct or not
hash(second 4-digit PIN + 128-bit random)
Confirm correct or not
Associate and starts EAP (Diffie-Hellman)
Brute forcing Wi-Fi Protected Setup
http://sviehb.files.wordpress.com/2011/12/viehboeck_wps.pdf

## Slide 49: Wireless Summary
Wireless is a big technology in this decade
Issues solved for wired returned for wireless
Wireless extremely limited in power, frequency, bandwidth
Topics not discussed, but are important
    Bluetooth
    RFID
    Security of dongles used to start cars
        Already broken <1 hour using brute force